## Slide 1: ICT4 Computer Architecture Experiment MIPS Laboratory

## Slide 2: Overview
I. Introduction to MIPS
II. MIPS programming model
III. MIPSIT user guide

## Slide 3: I. Introduction to MIPS
MIPS (originally an acronym for Microprocessor without Interlocked Pipeline Stages)
MIPS is a RISC (Reduced Instruction Set Computer) instruction set architecture (ISA) developed by MIPS Technologies (formerly MIPS Computer Systems, Inc.)
In 1981, a team led by John L. Hennessy at Stanford University started work on what would become the first MIPS processor.
Multiple revisions of the MIPS instruction set exist, including MIPS I, MIPS II, MIPS III, MIPS IV, MIPS V, MIPS32, and MIPS64.
http://en.wikipedia.org/wiki/MIPS_architecture

## Slide 4: Applications of MIPS processor

## Slide 5: Applications of MIPS processor

## Slide 6: Applications of MIPS processor

## Slide 7: II. MIPS Programming Model
Data Types
Registers
Instruction Formats
MIPS Instruction
Addressing Mode
MIPS Assembly program
MIPSIT

## Slide 8: Data Types
MiniMIPS registers hold 32-bit (4-byte) words. Other common data sizes include byte, halfword, and doubleword.
Byte = 8 bits
Word = 4 bytes
Doubleword = 8 bytes
Quadword (16 bytes) also used occasionally
Halfword = 2 bytes
Used only for floating-point data, so safe to ignore in this course

## Slide 9: Register Conventions
Figure 5.2 Registers and data sizes in MiniMIPS.

## Slide 10: Instruction Formats
A typical instruction for MiniMIPS and steps in its execution.

## Slide 11: MiniMIPS Instruction Formats
Figure 5.4 MiniMIPS instructions come in only three formats: register (R), immediate (I), and jump (J).

## Slide 12: Simple Arithmetic/Logic Instructions
Figure 5.5 The arithmetic instructions add and sub have a format that is common to all two-operand ALU instructions. For these, the fn field specifies the arithmetic/logic operation to be performed.
Add and subtract already discussed; logical instructions are similar
add $t0,$s0,$s1 # set $t0 to ($s0)+($s1)
sub $t0,$s0,$s1 # set $t0 to ($s0)-($s1)
and $t0,$s0,$s1 # set $t0 to ($s0)($s1)
or $t0,$s0,$s1 # set $t0 to ($s0)($s1)
xor $t0,$s0,$s1 # set $t0 to ($s0)($s1)
nor $t0,$s0,$s1 # set $t0 to (($s0)($s1))

## Slide 13: Arithmetic/Logic with One Immediate Operand
Figure 5.6 Instructions such as addi allow us to perform an arithmetic or logic operation for which one operand is a small constant.
An operand in the range [-32 768, 32 767], or [0x0000, 0xffff], can be specified in the immediate field.
addi $t0,$s0,61 # set $t0 to ($s0)+61
andi $t0,$s0,61 # set $t0 to ($s0)61
ori $t0,$s0,61 # set $t0 to ($s0)61
xori $t0,$s0,0x00ff # set $t0 to ($s0) 0x00ff
For arithmetic instructions, the immediate operand is sign-extended
1 0
0 1
Errors

## Slide 14: Load and Store Instructions
MiniMIPS lw and sw instructions and their memory addressing convention that allows for simple access to array elements via a base address and an offset (offset = 4i leads us to the i th word).
lw $t0,40($s3)
lw $t0,A($s3)

## Slide 20: Examples for Conditional Branching
If the branch target is too far to be reachable with a 16-bit offset
(rare occurrence), the assembler automatically replaces the branch
instruction beq $s1,$s2,L1 with:
bne $s1,$s2,L2 # skip jump if (s1)(s2)
j L1 # goto L1 if (s1)=(s2)
L2: ...
Forming if-then constructs; e.g., if (i == j) x = x + y
bne $s1,$s2,endif # branch on ij
add $t1,$t1,$t2 # execute the “then” part
endif: ...
If the condition were (i < j), we would change the first line to:
slt $t0,$s1,$s2 # set $t0 to 1 if i<j
beq $t0,$0,endif # branch if ($t0)=0;
# i.e., i not< j or ij

## Slide 22
The simple while loop: while (A[i]==k) i=i+1;
Assuming that: i, A, k are stored in $s1,$s2,$s3
Solution
loop: add $t1,$s1,$s1 # t1 = 4*i
add $t1,$t1,$t1 #
add $t1,$t1,$s2 # t1 = A + 4*i
lw $t0,0($t1) # t0 = A[i]
bne $t0,$s3,endwhl #
addi $s1,$s1,1 #
j loop #
endwhl: … #
while Statements
Example

## Slide 23
switch(test) {
case 0:
a=a+1; break;
case 1:
a=a-1; break;
case 2:
b=2*b; break;
default:
}
beq s1,t0,case_0
beq s1,t1,case_1
beq s1,t2,case_2
b default
case_0:
addi s2,s2,1 #a=a+1
b continue
case_1:
sub s2,s2,t1 #a=a-1
b continue
case_2:
add s3,s3,s3 #b=2*b
b continue
default:
continue:
Example
switch Statements
Assuming that: test,a,b are
stored in $s1,$s2,$s3
The simple switch

## Slide 25: Pseudoinstructions
Pseudoinstructions means “fake instruction”
Pseudoinstructions do not correspond to real MIPS instructions
The assembler, that converts assembly language programs to machine code, would then translate pseudoinstructions to real instructions, usually requiring at least one on more instructions.
Example:
  mov $rt, $rs #Copy contents of register s to register t, R[t] = R[s]
=> real instruction: addi $rt, $rs, 0
Notes: Pseudoinstructions not only make it easier to program, it can also add clarity to the program, by making the intention of the programmer more clear

## Slide 27: Procedure & Stack
Procedure call:
jal ( jump and link)
Return to call point
jr $ra

## Slide 28: Stack

## Slide 29: Stack

## Slide 30: $sp and $fp

## Slide 31: Example: $sp and $fp

## Slide 32: III. MIPSIT User Guide
MIPSIT IDE + MIPS Simulator
MIPS assembly program

## Slide 33: Instroduce to MIPSIT Studio
MIPSIT Studio: a tool to edit, compile and simulate programs based on MIPS instruction set.

## Slide 34: Installation
Extract MipsIt.rar to installed folder, “C:\MipsIt” for example. After this step, MipsIt folder will have following structure:
MipsIt\bin: include execution files, such as
  MipsIt.exe: an editor and compiler program
  Mips.exe: a simulator program
  MipsPipeS.exe: a simple pipeline simulator program
  MipsPipeXL.exe: a more complicated pipeline simulator program
…
MipsIt\include: include header files
MipsIt\lib: include library files
…

## Slide 35: IDE Basics

## Slide 36: IDE Basics
Files list
Editor
Compile, Build
Upload to Simulator

## Slide 37: The Simulator
MIPS.exe

## Slide 38: The Simulator
CPU View/modify the CPU registers. RAM View/modify memory, also referred to as the MemView. This unit has most functions of all, for a more detailed description see below. Console Standard input/output for programs that use it. I/O Simulates the 8-bit I/O unit, with 8 switches and 8 LEDs. D-Cache/I-Cache Views of the data and instruction caches. Interrupt Simulates the interrupt unit, with buttons K1, K2 and the timer.

## Slide 39: MIPSIT & MIPS
MIPSIT
MIPS
UPLOAD

## Slide 40: New project
Add files

## Slide 41
Chú ý: lỗi compile
  Kiểm tra File/Option
  Mục Compiler executable
  Trỏ đến $Root\MipsIT\bin\xgcc.exe
  (Không chứa dấu cách)

## Slide 42: MIPS assembly program
#include <iregdef.h>
.data
#declare variables
.text
.globl start
.ent start
start:
#main
.end start
.ent CTCon
CTCon:
#procedure
.end CTCon

## Slide 43: Example: Hello World
#include <iregdef.h>
.data
test: .asciiz "Hello World"
.text
.set noreorder
.globl start
.ent start
start:
la a0,test #load the address of test string to a0
jal printf #print test tring to console
.end start

## Slide 44: Pipelined MIPS

## Slide 45: Lab 3. Arithmetic & Logical Operation
Bit mask in logical operation
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
li s0,0x0563 #load test value for these function
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
andi t0,s0,0xff #Extract the LSB of s0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
s0 =
MASK
t0 =

## Slide 46: Lab 3. Arithmetic & Logical Operation
s1 xor s2 < 0
s1 < 0
s3 < s1
s3 < s1
t0 = 0
s3=s1+s2
t0 = 1
Overflow
EXIT:
No Overflow
TRUE
FALSE
TRUE
TRUE
FALSE
FALSE
TRUE
FALSE
Check overflow

## Slide 47: Lab 4. Procedure Calls, Assigment 4. n! (stack with n=3)
$ra(0)
$a0(0) = 3
$fp(0)
…..
$fp(0) ->
$sp(0) ->
$fp(1) ->
$sp(1) ->
$ra(1)
$a0(1) = 2
$fp(1)
$ra(0)
$a0(0) = 3
$fp(0)
…..
$fp(0) ->
$sp(0) ->
$fp(1) ->
$sp(1) ->
$ra(2)
$a0(2) = 1
$fp(2)
$ra(1)
$a0(1) = 2
$fp(1)
$ra(0)
$a0(0) = 3
$fp(0)
…..
$fp(0) ->
$sp(0) ->
$fp(1) ->
$sp(1) ->
$fp(2) ->
$sp(2) ->
$fp(2) ->
$sp(2) ->
$fp(3) ->
$sp(3) ->
Lần gọi 1 (a0=3)
Lần gọi 2 (a0=2)
Lần gọi 3 (a0=1)

## Slide 48: Lab 5. Character string
strcpy
L1:
add t1,s0,a1 #address of y[i] in t1
lb t2,0(t1) #t2=y[i]
add t3,s0,a0 #address of x[i] in t3
sb t2,0(t3) #x[i]=y[i]
beq t2,zero,L2 #if y[i]==0, go to L2
nop
addi s0,s0,1 #i=i+1
j L1 #go to L1
nop
L2:
Địa chỉ xâu y:
a1 = 800203c0
Địa chỉ xâu x:
a0 = 800203d5
s0=6, x[6]=y[6]
Ký tự ‘a’
s0=6, x[6]=y[6]
Ký tự ‘a’
Gõ trực tiếp ngăn nhớ giá trị địa chỉ muốn xem. ví dụ: 800203c0 (xâu y)